## Slide 1: Current Status of the Neutrinos Angra Experiment: Monitoring nuclear reactors with antineutrino detectors

## Slide 2: Motivations for ANGRA
Very interesting for the Brazilian science:
  Start experimental neutrino physics in Brazil
  taking advantage of existing antineutrino sources
  (Angra-I and II nuclear reactors).
  Possibility to do neutrino applied physics:
  . nuclear safeguards applications.
  . new detector technologies.
  Develop know how in experimental neutrino physics to be used in future projects.

## Slide 3
CBPF
J.C. Anjos, G.L. Azzi, H. Lima Jr, M. Vaz,
Collaborators:
Aridio Schiapazza
Rogério M. da Silva
Graduate Students: Marcelo Nascimento Souza (PhD)
Thamys Abrahão (MSc)
Marcio Nunes (PhD)
Rafael Gama (PhD)
Undergraduate Students: Upiratan Machado (UERJ)
Beatriz Santos (UERJ)
Igor Oliveira (IME)
Brazilian Institutions:
ANGRA Collaboration:
Notes: 3

## Slide 4: ANGRA Collaboration:
4
PUC-RJ
Hiroshi Nunokawa
UNICAMP
E. Kemp, T. Bezerra, L. F. González, L. M Santos
UFBA
Iuri M. Pepe
Paulo Farias
UEFS
Germano P. Guedes
UFABC
Marcelo Leigui, P. Chimenti
UFJF
Luciano M. Andrade, Rafael A. Nóbrega,
Augusto S. Cerqueira
Unifal
Gustavo Valdiviesso
Notes: 4

## Slide 5
Nuclear Safeguards Applications
ANGRA PROJECT:
Notes: 5

## Slide 6
6
ANGRA PROJECT:
DESIGN GUIDELINES:
Follow recommendations of the
2008 IAEA Expert’s Workshop
Notes: 6

## Slide 7
DESIGN GUIDELINES:
Focused Workshop on Antinu-e Detection for SG Applications (2008)
Notes: 7

## Slide 8: Why IAEA may have interest in antineutrino detectors?
Antineutrinos can not be shielded and are produced in very large amounts in nuclear reactors
(~ 1020 antineutrinos/s)
Antineutrinos coming from different isotopes have different energy spectrum: antineutrino measurement may reveal, in principle, fissile composition of nuclear fuel.
Non-intrusive, Real Time, Remote reactor monitoring: thermal power & fissile material
Search for new methods on safeguards verification

## Slide 9
International Cooperation CNEN/DOE
2012 Agreement
Notes: 9

## Slide 10
International Cooperation CNEN/DOE
2012 Agreement
Notes: 10

## Slide 11: New challenge: neutrino detection above ground
Angra Neutrino laboratory: 40’ container

## Slide 12
Angra detector facts: Water Cherenkov
Prompt signal:
Positron 1 ~ 12MeV
Delayed signal:
γ’s from neutron capture
on Gd: 8MeV
Time interval: Δt ~ 30μsec
Reactor power: 4 GWth
Target mass: 1 ton
Detector distance to core: ~25 meters
Inverse beta decay interactions per day: ~5,000

## Slide 13
Monitoring nuclear reactors with antineutrinos
Observed  spectrum
 flux from the reactor
Inverse -decay
cross section
The observed energy spectrum is the result of the antineutrino flux emmited weighted by the antineutrino-proton cross section

## Slide 14
14
New Detector Design
Detector design (2011)
(detector + muon veto)
Central detector: water tank with 32 PMTs to detect Cherenkov radiation
external water shieldTs
Notes: 14

## Slide 15
The neutron detector: 260 l prototype for neutron detection in Gd loaded water ( 1 PMT)
252Californium Source arrived at CBPF in June 2012
Instalation of a small laboratory in the old CBPF linear accelerator tunnel;
Authorization to use the neutron source given by CNEN in 2011;
Instalation of water purification station concluded;
Experimental measurements started with pure water:
Calibration with Cosmic muons finished;
Next step: add Gadolinium in the water

## Slide 16: ELECTRONICS STATUS

## Slide 17
Front-end electronics
VME bus
PMT
ADC
125 MHz
trigger logic
control and status registers
data builder
TDC
81 ps
28 bits
stop
start*
time encoding
FPGAs
* trigger pulse from previous event
leading-edge
discriminator
control
data
addr
signal conditioning
10 bits
FIFO
DC level-1
trigger
Eletronics Design - (conceptual diagram 2007)
DAQ diagram
Notes: 17

## Slide 18: VME 6U Board: DAQ: waveform digitizer + time stamp
Lay-out of VME board developed in collaboration with Brazilian industry CADSERVICE
Components mounted by CADSERVICE (Campinas, SP)
Eletronics Design - (present status 2012)
Notes: 18

## Slide 19: VME 6U Board waveform digitizer + time stamp
30 units produced and tested.
Data acquisition with several
modules being tested
Eletronics Design - (present status 2012)
Notes: 19

## Slide 20: Data Acquisition
Data readout (software)
Readout software code developped in C and ADA
3 fully working systems, each one with one ROPs + NDAQs (2 at CBPF e 1 at Unicamp)
Last firmware and DAQ software version is very stable, working without problems for few days continusly in lab tests.
All software is SVN version controled.
Last implemented code has a check of the serial number and firmware version at the startup in the DAQ-level.

## Slide 21: Front-end Electronics - UFJF
4 stages operational amplifier
8 channels circuit using NIM standard module.
5 boards (PCB) built in July/2012 and are now been mounted.

## Slide 22: Optimized Digital Detection for the Trigger System.
Luciano M. de A. Filho (UFJF)
Augusto Santiago (UFJF)
A. F. Barbosa (CBPF)

## Slide 23: Proposal
23
Digital
Filter
Trigger
Decision
Central FPGA of NDAQ
ADC
Digital Filter to maximize signal/background ratio before the trigger.
Implementation → Filter FIR.
Two methods tested
  Matched Filter.
  Optimized Filter for amplitude estimate.
Similar results for both filters.
Optimized filter has advantage of output in Volts.
Increase signal/background
ratio

## Slide 24: Results
24
Peak/Valley = 2.5
Peak/Valley = 5.0
Variance of the measurement:
Error in the measurement:
ANTES
DEPOIS

## Slide 25: Detector Simulation Studies

## Slide 26: Data Analysis: simulation of expected signal and background
Signal and background Simulation:
Positrons (from neutrino interaction)
Neutrons (from neutrino interaction)
Cosmic ray induced background

## Slide 27
Signal and cosmic background frequency
Table 1: Particles from antineutrino signal
Table 2: Particles from cosmic background
Particles | Frequency (HZ)
Muons | 210±6
Neutrons | 20±1
Protons | 2.0±0.2
Pions | 0.40±0.01
Photons | (8 ± 1)×103
Positrons | 257±61
Electrons | 242±140
Particles | Frequency (HZ)
Positrons | 0.060±0.001
Neutrons | 0.060±0.001

## Slide 28: Muons, neutrons, protons, pions, photons, positrons and electrons

## Slide 29: Particle frequency density from antineutrino signal

## Slide 30
Signal and cosmic background frequency
(10-200 P.E)
Table 1: Particle from antineurino signal
Table 2: Particles from cosmic background
Particles | Frequency (HZ) 10-200 P.E
Positrons | 0.050±0.001
Neutrons | 0.050±0.001
Particles | Frequency (HZ) 10-200 P.E
Muons | 12±1
Neutrons | 13±1
Protons | 0.44±0.09
Pions | 0.048±0.004
Photons | (5.7 ± 1.1)×103
Positrons | 158±48
Electrons | <186 (90% C.L)

## Slide 31
Study of Gadolinium concentration
Delayed coincidence for 0.1, 0.5 and 1.0% Gd
Stopping muons and spallation neutrons for 0.1, 0.5 and 1.0% Gd

## Slide 32
Study of shielding
Table 1: Cosmic neutron events
Table 2: Cosmic muons events: 10,000 generated
Shielding | Neutrons simulated
Polyethylene | 10.000
Water | 10.000
Neutrons detected | Neutrons with signal delayed
299 | 153
282 | 98
Shielding | Muons signal delayed
Polyethylene | 56
Water | 59
Spallation neutrons | Muons with multi-neutrons
28 | 5
17 | 1
Shielding | Fake signals
Polyethylene | 8
Water | 6
Frequency (Hz)
1.3±0.5
1.0±0.4
Table 3: Muons events

## Slide 33: Data acquisition simulation
Simulated data for one day of data taking and data reduction by each selection criteria
  Generated events per day:
  Muons ~ 30,000,000
  Cosmic neutrons ~ 340,000
  Positrons from inv. Beta decay ~ 5,250
  Neutrons from inv. Beta decay ~ 5,250
EXPECTED RATES AT THE DETECTOR
Neutrino interactions: ~ 5,250/day ( ~ 0.06 Hz)
Muon rate at target: ~ 350 Hz
Cosmic ray induced neutron rate: ~ 70 Hz (no shielding)
Cosmic neutron background: ~ 4 Hz (30cm polyethylene)
 background rate must be reduced by factor ~104

## Slide 34: Data acquisition simulation
  Selection criteria:
  Muon identification by external veto: 98% efficiency
  Energy cut > 100 photo electrons (p.e.)
  Up/down photo electron ratio < 0.05
  Time window between events 0 – 300 µs
  Time window between events 150 – 300 µs (background fit)
  Time window between events 0 – 100 µs (signal fit)
Simulated data for one day of data taking and data reduction by each selection criteria

## Slide 35: Data acquisition simulation
Fit functions:
Background: linear fit in time interval 150 – 300 µs
Signal: exponential (0 - 100 µs ) + linear (background)

## Slide 36: DETECTOR STATUS

## Slide 37: DETECTOR STATUS
Arrival of water shielding
vessels at CBPF
July 2012

## Slide 38: DETECTOR STATUS
Checking detector vessels
Starting tests at CBPF

## Slide 39: DETECTOR STATUS
Mounting Active shielding
Covering internal walls with Tyvek
and installing PMTs

## Slide 40
Status of the Neutrinos ANGRA project
New 40’ High Cube container: deployed in Angra
Geant4 simulation of detector response to
signal and background events: working
- Neutrino signal extraction – simulated
New detector design: active water shield
Water shielding and target vessels: built
Front-end electronics: been tested
Electronics for DAQ: ready
Data acquisition software: ready
Detector test at CBPF: July 2012
- Deployment in Angra: begining 2013

## Slide 41
New Detector Technologies
ANGRA PROJECT
Notes: 41

## Slide 42
42
New proposal:
Neutrino coherent scattering
detection at Angra
Notes: 42

## Slide 43
43
Coherent neutrino-nucleous interaction
is a fundamental interaction predicted by
the standard model whose X-section, for Eν < 50 MeV, is expressed by
N2  σtot Very High
It has never been observed !!
Notes: 43

## Slide 45
45
CCD detectors present low electronic noise
and can register nuclear recoil!
Hard to observe process
Detector should:
1) be able to distinguish nuclear recoil
2)present extremely low electronic noise
CCD (Charged Coupled Device)
are silicon detectors that convert photons in
electrons generating a current that can be
quantified by an ADC
Notes: 45

## Slide 46
46
DAMIC CCD:
- CCD are readout serially
(2 output for 8 million pixels)
- Very low noise level ~7.2 eV
- 1 g per CCD - 18 cm2
- 250 m thick
CCD detectors have been used in dark energy and
dark matter experiments like DES (Dark Energy
Survey) and DAMIC (Dark Matter in CCD).
CCD detectors are potential candidates
for experiments aimed at observing
coherent neutrino-nucleous interactions.
Notes: 46

## Slide 47
47
MUONS
ELECTRONS
DIFFUSION LIMITED HITS
Nuclear recoils produce diffusion limited hits
How radiation shows in CCDs
Notes: 47

## Slide 48
48
Lab-A (Fermilab)
MINOS cave (100 m
underground)
MINOS + lead shield
Notes: 48

## Slide 49
CONNIE FACTS
Number of CCD detectors: 10
Total mass: 10 g
Reactor thermal power: 4 GW
Detector distance from reactor core: 30 m
Anti-neutrino flux at the detector: ~7 x 1012 cm-2 s -1
Event rate : ~1 event every 4 days
Shielding and noise reduction are the critical factors.
Development of noise reduction techniques in the core of the project.

## Slide 50
CCD – Angra detector
Box with 2 CCD for the
CONNIE experiment
Vessel design with shield

## Slide 51
51
Final remarks
Most of the CONNIE detector ready at FERMILAB.
R&D needed to reduce noise. Two possible techniques under consideration to be used in the project ( G. Cancelo):
  Digital signal processing techniques for noise reduction
  New CCD architecture (Skipper CCD)
Angra-CCD neutrino detector will first be assemble at CBPF,
tested and only then reassembled in Angra.
CBPF-Angra link (for remote data acquisition) working.
Ge detector + associated equipment and lead shield available at CBPF for all background studies needed.
Good opportunity to develop new detector technology and advance CCD detectors technology.

## Slide 52
Developing Know How for
Future Experiments
ANGRA PROJECT
Notes: 52

## Slide 53
ANDES UNDERGROUND LABORATORY

## Slide 55
THANK YOU

## Slide 56: Publicações

## Slide 57: Publicações